## Slide 1: APPENDIX 3 - Proposed A29 Road Improvements
Extend 30mph speed limit south to Bury Gate junction
Bury Gate junction
Buff colour road-edge throughout - buffers narrow footway - encourages active travel
Add 30 mph reminder roundels on road
Extend ‘no overtaking’ lines throughout - but omit on buff sections
remove cats’ eyes throughout 30 zone
Throughout 30mph zone
New 300m (2x150m) 20 mph school zone, to include buff colour section
20 mph signage/roundels
St James’ primary school
Reduce National Speed Limit between Pulborough & Coldwaltham rail bridge to 40mph – clear/widen roadside footway from Pulborough
Start 30mph section north of rail bridge
Coldwaltham rail bridge
Village entry gates – reinforce 30mph
Buff colour bands across road
Buff colour road-edge ends at gates
Watersfield village entry
Buff colour section at Greatham Lane/Waltham Park Rd junction, with improved signage
Footway clearance, community-led, WSCC help
Fixed speed camera opposite Lodge Hill
Between Coldwaltham & Watersfield
Village entry gates – reinforce 30mph
Buff colour bands across road
Buff colour road-edge starts at gate
Coldwaltham village entry
north south in Coldwaltham Parish
Watersfield
Buff colour section at River Lane / Sandy Lane junction’ - with planters